## Slide 1
LEPL KUTAISI INTERNATIONAL UNIVERSITY
School of Computer Science · Bachelor Program of Computer Science
C0 to Machine Code
Assembler, Simulator and Basic OS Support
Mirian Shilakadze · Mikheili Kvinikadze · Konstantine Machavariani
Thesis Supervisor: Prof. Dr. Walter Tichy Co-supervisor: Prof. Dr. Wolfgang J. Paul
Bachelor's Thesis Defense · Kutaisi, 2026

## Slide 2
INTRODUCTION
From C0 Source to a Running Kernel
Started from an existing C0-to-MIPS compiler (Pirtskhelani & Khotchava, KIU)
Added a standalone assembler: MIPS assembly → bytecode
Extended C0 into a “C0 + Assembly” dialect for OS-level programming
Built a MIPS simulator to debug the translation pipeline
Implemented a minimal OS kernel — bootloader and runvm — targeting an FPGA board
C0 + Assembly
source
Compiler
Assembler
Bytecode
Bootloader
Kernel
on FPGA
C0 to Machine Code — Bachelor's Thesis
2

## Slide 3
INTRODUCTION
Author Contributions & Scope
Chapter | Topic | Author
3 | MIPS Assembler | Mirian Shilakadze
4, 6 | Compiler Extensions (“C0 + Assembly”) & OS Kernel | Mikheili Kvinikadze
5 | Instruction Simulator | Konstantine Machavariani
Scope & Limitation
The kernel and bootloader were verified only through simulation. The FPGA hardware designs for disk access, interrupt handling, and the MMU were not finalized in time, so on-board testing was not possible.
C0 to Machine Code — Bachelor's Thesis
3

## Slide 4
MIPS ISA
Machine Configuration
pc ∈ 𝔹³²
program counter — points to the instruction to be executed
gpr : 𝔹⁵ → 𝔹³²
32 general-purpose registers; register 0 is hard-wired to zero
m : 𝔹³² → 𝔹⁸
byte-addressable processor memory
I(c) = c.m⁴(c.pc)
current instruction — 4 bytes fetched at the program counter
Visible Data Structures
pc (32 bits)
gpr[0..31]
32 × 32-bit registers
memory m
2³² bytes, byte-addressable
C0 to Machine Code — Bachelor's Thesis
4

## Slide 5
MIPS ISA
Three Instruction Formats
opc (6)
rs (5)
rt (5)
imm (16)
I-type
opc (6)
opc (6)
rs (5)
rt (5)
rd (5)
sa (5)
fun (6)
R-type
opc (6)
opc (6)
iindex (26)
J-type
opc (6)
The 6-bit opcode (bits 31–26) determines the instruction's type
I-type
data transfer & branches — lw, sw, addi, beq, bltz …
R-type
register-to-register ops & jumps — add, sub, and, jr, jalr, sysc …
J-type
unconditional jumps with a pc-relative offset — j, jal
C0 to Machine Code — Bachelor's Thesis
5

## Slide 6
ASSEMBLER
Single-Pass Design
Goal: translate MIPS assembly into bytecode in a single pass
Emit bytecode as early as possible — avoid buffering the whole program
Every non-blank input line is one of three forms:
  Instruction
  Macro invocation
  Label definition
Example assembler input
macro: gpr(30) = enc(10240, uint)
macro: gpr(28) = enc(5120, uint)
addiu 29 28 16
subu 1 29 28
srl 1 1 2
macro: zero(28, 1)
j _main
_main:
addi 1 28 0
macro: gpr(2) = enc(2, int)
sw 2 1 0
C0 to Machine Code — Bachelor's Thesis
6

## Slide 7
ASSEMBLER
Instruction Registry
A factory pattern avoids large switch statements over 20+ mnemonics
Each mnemonic is registered declaratively with its encoder, syntax and operand parsing rule
The assembler queries the registry for opcode lookup, operand parsing, and argument ordering
The same registry is reused later by the simulator (Slide 17)
InstructionRegistry.java (excerpt)
public class InstructionRegistry {
Map<String, InstructionCreator>
encoderInstructionMap =
Initializer.initializeEncoderMap();
Map<String, InstructionCreator>
executableInstructionMap =
Initializer.initializeExecutableMap();
static Instruction createForEncoder(
String mnemonic, int[] operands) {...}
static Instruction createForExecutor(
String mnemonic, int[] operands) {...}
}
C0 to Machine Code — Bachelor's Thesis
7

## Slide 8
ASSEMBLER
Forward References & the Drain Routine
A label used before its definition leaves the instruction “unresolved”
Because output is streamed in order, every following instruction must wait too
Unresolved instructions are queued; drainInstructions() emits everything that has become resolved after each line
Labels defined before use are resolved — and emitted — immediately
Forward reference example
j _loop # forward-refers to _loop
addi 2 2 1 # deferred until _loop is known
_loop:
subu 3 3 3
jr 31
drainInstructions() — pseudocode
WHILE queue IS NOT EMPTY:
instr = queue.PEEK()
IF NOT instr.isResolved(): BREAK
queue.POP()
emit(instr)
C0 to Machine Code — Bachelor's Thesis
8

## Slide 9
ASSEMBLER
Macro Instructions
A macro groups a reusable set of MIPS instructions behind one line of assembly
Expanded into its full instruction sequence at translation time
Kept in a single class, Macros.java, one expansion routine per pseudo-instruction
gpr(i) = enc(val, type)
Evaluate a constant value into register i (lui + ori)
zero(i, j)
Zero j memory words starting at address gpr(i)
mul / divu / divt(k, i, j)
Software multiply / unsigned / signed divide
ssave(r) / srestore(r)
Save / restore a register to scratch memory
restore-user / save-user
Switch a virtual user's configuration in/out
C0 to Machine Code — Bachelor's Thesis
9

## Slide 10
C0 + ASSEMBLY
Why Extend C0?
Kernel code needs two things plain C0 cannot express:
  direct access to registers
  access to memory outside the range of C0 variables
Two additions close this gap:
  Register read/write — gpr(i) = id {J} and id = gpr(i) {J}
  Inline assembly — asm(MIPS)
J lists registers that must stay unchanged while translating the statement
OS primitives such as copyms and readdisk return nothing — this motivated adding void functions too
C0 to Machine Code — Bachelor's Thesis
10

## Slide 11
C0 + ASSEMBLY
Grammar Extensions
Reading & writing registers
<NuS> -> <DiS> | <DiS>,<NuS>
<St> -> ... | <id>=gpr(<DiS>)
| <id>=gpr(<DiS>) {<NuS>}
| ... | gpr(<DiS>)=<id>
| gpr(<DiS>)=<id> {<NuS>}
Inline assembly
<DiLeCC> -> - | <DiLe>
<DiLeCCS> -> <DiLeCC> | <DiLeCCS><DiLeCC>
<ASM> -> <DiLeCCS> | <ASM> <DiLeCCS>
<St> -> ... | asm( <ASM> )
“gpr” and “asm” are added to the terminal symbols
<DiLeCC> extends digits/letters with “−”, needed for negative lw/sw offsets
<ASM> concatenates arbitrary space-separated tokens — broad, but sufficient for kernel assembly
C0 to Machine Code — Bachelor's Thesis
11

## Slide 12
C0 + ASSEMBLY
Keeping the Grammar LR(1)
Any grammar change risks breaking LR(1) parsability — checked with the DK1 test
Parser generation itself was left unchanged; the same DK1 automaton construction applies
The first attempt at adding inline assembly failed the test:
R1: <ASM> -> <DiLeCCS>
R2: <ASM> -> <DiLeCCS> . <ASM>
Both rules share look-ahead symbol “ ” (space), which fails the accept-state condition of the test
Fix: invert the derivation order → <ASM> -> <DiLeCCS> | <ASM> <DiLeCCS>
C0 to Machine Code — Bachelor's Thesis
12

## Slide 13
C0 + ASSEMBLY
Translating Register Reads & Writes
generateStS inspects the border word of each statement and dispatches to:
  generateReadGPR, generateWriteGPR, generateInlineAsm
Registers named in J (plus the target register) are occupied during translation, then freed
Inline assembly needs no further translation — its MIPS text is copied straight into the instruction stream
id = gpr(i) {J} — translation flow
id
evaluateId
varRegId
sw i, varRegId.reg, 0
C0 to Machine Code — Bachelor's Thesis
13

## Slide 14
C0 + ASSEMBLY
Void Functions
OS primitives (copyms, readdisk, writedisk) don't return a value — C0 needed void functions
Grammar: void f(params){locals; body} — same shape as a regular function, minus the return type
generateCodeVoidFunction:
  store return address on the stack
  translate the function body
  restore the stack pointer, then jr back to the caller
This change added no overhead to the DK1 test
Function-call stack frame
Vars
Pars
ra
top / caller frame
C0 to Machine Code — Bachelor's Thesis
14

## Slide 15
C0 + ASSEMBLY
Example: writems & copyms
C0 + Assembly source
void writems(uint x, uint a){
gpr(1) = x;
gpr(2) = a {1};
asm( sw 1 2 0 )
}
Generated MIPS
_writems:
sw 31 29 -12
addi 1 29 -8
lw 1 1 0
addi 2 29 -4
lw 2 2 0
sw 1 2 0
lw 1 29 -12
jr 1
writems(x, a)
stores value x in main memory at address a
copyms(a, b, L)
copies L consecutive words from a to b — built the same way, with a loop of asm() statements
Both are used directly by the kernel's disk-access routines
C0 to Machine Code — Bachelor's Thesis
15

## Slide 16
C0 + ASSEMBLY
Bugs Found in the Existing Compiler
1
Macro-aware branch offsets
Conditional statements (while, if, if-else) computed branch offsets by counting each macro as a single instruction. Fixed by tracking each macro's real expanded length.
2
32-bit constant loading
addi (16-bit immediate) was used for large constants and silently truncated them. Replaced with the gpr()=enc() macro (lui + ori).
3
Array element access
Base address, element type, and displacement for id[e] were computed incorrectly; all three were reviewed and corrected.
C0 to Machine Code — Bachelor's Thesis
16

## Slide 17
SIMULATOR
A Purpose-Built MIPS Simulator
General-purpose tools (e.g. MARS) don't match our custom ISA subset, macros, or label syntax
Built as a debugging aid for the translation pipeline — not a formal proof of correctness
All machine state lives in one Configuration object:
  pc — modeled as a 64-bit long (Java has no unsigned 32-bit type)
  gpr[32] — register 0 writes are always ignored
  paged memory — see next slide
Configuration.java (excerpt)
public class Configuration {
private long pc;
private final int[] gpr;
private final Map<Integer, byte[]>
memoryPaged;
private boolean isRunning;
public Configuration() {
this.pc = 0L;
this.gpr = new int[32];
this.isRunning = true;
}
}
C0 to Machine Code — Bachelor's Thesis
17

## Slide 18
SIMULATOR
Sparse, Paged Memory Model
A full 2³²-entry array is not practical to allocate
Memory is modeled as 4 KB pages inside a HashMap<Integer, byte[]>
A page is created only the first time a program writes into it
Address = page id (upper 20 bits) + offset (lower 12 bits)
A read to a never-written page returns zero — matching real zeroed memory
getWord — packing 4 bytes into a word
int getWord(int address) {
return
((getByte(address) & 0xFF)<<24) |
((getByte(address+1) & 0xFF)<<16) |
((getByte(address+2) & 0xFF)<<8) |
(getByte(address+3) & 0xFF);
}
& 0xFF masks each byte — otherwise Java sign-extends it on promotion
>>> (unsigned shift) is used in setWord to avoid dragging the sign bit along
C0 to Machine Code — Bachelor's Thesis
18

## Slide 19
SIMULATOR
Fetch – Decode – Execute
c′ = δ(c, 0)
— one simulation step implements the ISA's transition function
The loop runs until a syscall halts the machine, or instructions run out
Fetch
I(c) = c.m⁴(c.pc)
Read the 32-bit word at pc
Decode
opc = I(c)[31:26]
6-bit opcode selects R/I/J handling
Execute
operands parsed → Instruction
Registry lookup → execute(config)
repeat until syscall / halt
C0 to Machine Code — Bachelor's Thesis
19

## Slide 20
SIMULATOR
Testing the Full Pipeline
Over 70 self-verifying C0 test programs: integer/unsigned arithmetic, pointers, structs, loops, conditionals, recursion
Each program ends with return 1, halted via a syscall — a clear, checkable exit
JUnit automates each test:
1
Compile C0 → MIPS bytecode
2
Create a fresh Configuration
3
Load bytecode into memory
4
Run simulate()
5
Assert registers & memory match expected values
C0 to Machine Code — Bachelor's Thesis
20

## Slide 21
OS SUPPORT
Bootloader + runvm
Goal: run multiple virtual users' programs on the target FPGA board
bootloader
detects the reset signal, fetches translated kernel code from disk
runvm
kernel primitive that runs a virtual user and transparently handles invalid-page-fault interrupts
Kernel main loop
[...] // initialize data structures
while true {
scheduler();
runvm()
}
reset ?
yes
no
fetch translated
kernel from disk
jump into the
middle of runvm
C0 to Machine Code — Bachelor's Thesis
21

## Slide 22
OS SUPPORT
Host Memory Layout
hd-ports
56K – 64K
two pages mapped to disk ports
upbase
44K – 52K
users' virtual pages (page-fault region)
heap
36K – 40K
reserved for kernel heap variables
stack
24K – 32K
kernel data structures & function frames
kernel
12K – 20K
translated kernel code (~1,629 instructions)
scratch
4K – 8K
saving/restoring register contents
ROM
0 – 4K
bootloader; only region present at start-up
C0 to Machine Code — Bachelor's Thesis
22

## Slide 23
OS SUPPORT
Page Tables, Process Control Blocks & Scheduling
PTA
flat array holding every user's page table
PTOI
per-user starting offset into PTA
PCB[i]
saved gpr / spr for user i — restored by runvm on every switch
Scheduling: simple round-robin over the p user processes
scheduler()
void scheduler(){
if (CP==p) {CP = 1u}
else {CP = CP+1u}
};
Address-translation setup (excerpt)
typedef uint[PTASIZE] PTAt;
typedef uint[p+1] PTOIt;
PTAt PTA; PTOIt PTOI;
i = 1u;
while i<p+1u {
PTOI[i] = (i-1u)*PTL;
i = i + 1u
};
C0 to Machine Code — Bachelor's Thesis
23

## Slide 24
OS SUPPORT
Switching Modes & Loading the Kernel
runvm
restore-user → run → save-user on interrupt → detect ipf via the exception-cause register → ipfHandler() → restore-user again
bootloader
on reset, FetchKernel.c0 reads kernel pages from disk into a fixed memory region; otherwise it jumps straight into the middle of runvm
MIPS uses pc-relative jumps, so jump targets are computed as offset = target − current pc
Fetching kernel code from disk
SPX = 0u;
PPX = a/4096u;
L = (b-a+4u)/4096u;
while L>0u {
readdisk(PPX, SPX);
SPX = SPX + 1u;
PPX = PPX + 1u;
L = L-1u
};
C0 to Machine Code — Bachelor's Thesis
24

## Slide 25
CONCLUSION
Limitations, Future Work & References
Limitations
Never tested on real FPGA hardware — disk, interrupts and MMU designs were not finalized in time
Kernel intentionally minimal: round-robin scheduling, only invalid-page-fault interrupts handled
Fixed-size kernel data structures — more users require editing kernel source directly
Future Work
Deploy and verify the kernel on the physical FPGA board
Extend the C0 compiler to cover more language features
Recognize a wider set of standard MIPS pseudo-instructions in the assembler
References
W. J. Paul, C. Baumann Petro, L. Sabine Schmaltz, System Architecture: An Ordinary Engineering Discipline, 2016
T. Pirtskhelani, I. Khotchava, Compiler Development for LR(1) Grammars: DK1 Test, Parsing, and Code Generation with Application to the C0 Language
M. Sipser, Introduction to the Theory of Computation, 3rd ed.
K. Vollmar, P. Sanderson, MARS: MIPS Assembler and Runtime Simulator
Thank you